INTERNATIONAL ORGANISATION FOR STANDARDISATION

ORGANISATION INTERNATIONALE DE NORMALISATION

ISO/IEC JTC1/SC29/WG11

CODING OF MOVING PICTURES AND AUDIO

ISO/IEC JTC1/SC29/WG11/N10826

July 2009, London, UK

| Source: | Audio |
| --- | --- |
| Title: | ISO/IEC 14496-3:200X/PDAM 2 – ALS Simple Profile and Transport of SAOC |
| Status: | Approved |

This document specifies the second amendment to ISO/IEC 14496-3:200X.

© ISO/IEC 2009 – All rights reservedISO/IEC 14496-3:200X/PDAM 2 56Part 3: Audio, AMENDMENT 2: ALS simple profile and transport of SAOCInformation technology — Coding of audio-visual objects Information technology — Coding of audio-visual objects — Part 3: Audio, AMENDMENT 2: ALS simple profile and transport of SAOCE2009-07-3(30) CommitteeISO/IECISO/IEC J200X2AmendmentInternational Standard2009 ISO/IEC 14496ISO/IEC 14496-3ISO/IEC 14496-3/PDAM 2  Coding of audio, picture, multimedia and hypermedia informationInformation technology11291 2Heading 2,H2,H21,Œ©o‚µ 2,h2,?co??E 2,뙥2,?c1,?co?ƒÊ 2,?2,Œ1,Œ2,Œ©2,DO NOT USE_h2,título 2,Œ©1,Œ©_o‚µ 2,2,Header 2,2nd levelHeading 1    02 STD Version 2.1c230   4C:\Users\ogura\Desktop\14496-1PDAM4.doc            ISO/IEC JTC 1/SC 29 N

Date:   2009-07-3

ISO/IEC 14496-3:200X/PDAM 2

ISO/IEC JTC 1/SC 29/WG 11

Secretariat:

Information technology — Coding of audio-visual objects — Part 3: Audio, AMENDMENT 2: ALS simple profile and transport of SAOC

Warning

This document is not an ISO International Standard. It is distributed for review and comment. It is subject to change without notice and may not be referred to as an International Standard.

Recipients of this draft are invited to submit, with their comments, notification of any relevant patent rights of which they are aware and to provide supporting documentation.

Copyright notice

This ISO document is a working draft or committee draft and is copyright-protected by ISO. While the reproduction of working drafts or committee drafts in any form for use by participants in the ISO standards development process is permitted without prior permission from ISO, neither this document nor any extract from it may be reproduced, stored or transmitted in any form for any other purpose without prior written permission from ISO.

Requests for permission to reproduce this document for the purpose of selling it should be addressed as shown below or to ISO's member body in the country of the requester:

[Indicate the full address, telephone number, fax number, telex number, and electronic mail address, as appropriate, of the Copyright Manger of the ISO member body responsible for the secretariat of the TC or SC within the framework of which the working document has been prepared.]

Reproduction for sales purposes may be subject to royalty payments or a licensing agreement.

Violators may be prosecuted.

Foreword

ISO (the International Organization for Standardization) and IEC (the International Electrotechnical Commission) form the specialized system for worldwide standardization. National bodies that are members of ISO or IEC participate in the development of International Standards through technical committees established by the respective organization to deal with particular fields of technical activity. ISO and IEC technical committees collaborate in fields of mutual interest. Other international organizations, governmental and non-governmental, in liaison with ISO and IEC, also take part in the work. In the field of information technology, ISO and IEC have established a joint technical committee, ISO/IEC JTC 1.

International Standards are drafted in accordance with the rules given in the ISO/IEC Directives, Part 2.

The main task of the joint technical committee is to prepare International Standards. Draft International Standards adopted by the joint technical committee are circulated to national bodies for voting. Publication as an International Standard requires approval by at least 75 % of the national bodies casting a vote.

Attention is drawn to the possibility that some of the elements of this document may be the subject of patent rights. ISO and IEC shall not be held responsible for identifying any or all such patent rights.

Amendment 2 to ISO/IEC 14496-3:200X was prepared by Joint Technical Committee ISO/IEC JTC 1, Information technology, Subcommittee SC 29, Coding of audio, picture, multimedia and hypermedia information.

Information technology — Coding of audio-visual objects — Part 3: Audio, AMENDMENT 2: ALS simple profile and transport of SAOC

In the following, changes in existing text and tables are highlighted by gray background.

In subclause 1.2 Normative references, add:

ISO/IEC 23003-2, Information technology — MPEG audio technologies — Part 2: Spatial Audio Object Coding

In subclause 1.3 Terms and Definitions, add:

SAOC: Spatial Audio Object Coding

and increase the index-number of subsequent entries.

In subclause 1.5.1.1 Audio object type definition, amend Table 1.1 with the updates in the table below:

| Object Type ID | Audio Object Type | Remark |
| --- | --- | --- |
|  | … |  |
| 42 | (reserved) |  |
| 43 | SAOC |  |
| 44-95 | (reserved) |  |

After subclause 1.5.1.2.37 add the following subclauses:

1.5.1.2.38 SAOC object type

The SAOC object type conveys Spatial Audio Object Coding side information (see ISO/IEC 23003-2) in the MPEG-4 Audio framework.

In subclause 1.5.2.1 (Profiles), add:

14. The ALS Simple Profile contains the audio object type 36 (ALS).

In subclause 1.5.2.1 (Profiles), Table 1.3 (Audio Profiles definition), add:

| Object Type ID | Audio Object Type | … | ALS Simple Profile |
| --- | --- | --- | --- |
| … | … | … | … |
| 36 | ALS | … | X |
| … | … | … | … |
| 42 | (reserved) |  |  |
| 43 | SAOC |  |  |

In subclause 1.5.2.3 (Levels within the profiles), add:

- Levels for the ALS Simple Profile

Table 1.13B – Level for the ALS Simple Profile

| Level | Max. number of channels | Max. sampling rate [kHz] | Max. word length [bit] | Max. number of samples per frame | Max. prediction order | Max. BS stages | Max. MCC stages |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 2 | 48 | 16 | 4096 | 15 | 3 | 1 |

The BGMC tool and the RLS-LMS tool are not permitted. Floating-point audio data is not supported.

In subclause 1.5.2.4 (audioProfileLevelIndication), insert the following new entry into Table 1.14 (audioProfileLevelIndication values) and adapt the “reserved for ISO use” range accordingly:

| Value | Profile | Level |
| --- | --- | --- |
| … |  |  |
| 0x3C | ALS Simple Profile | L1 |
| 0x3D - 0x7F | reserved for ISO use | - |
| … |  |  |

[Editor's note: In the case that SAOC profiles and levels are being defined, it should be considered to include them in the above table]

In subclause 1.6.2.1 extend Table1.15 “AudioSpecificConfig()”as follows:

Table 1.15 – Syntax of AudioSpecificConfig()

| Syntax | No. of bits | Mnemonic |
| --- | --- | --- |
| AudioSpecificConfig () |  |  |
| { |  |  |
| … |  |  |
| case 40: |  |  |
| case 41: |  |  |
| SymbolicMusicSpecificConfig() |  |  |
| break; |  |  |
| case 43: |  |  |
| saocPayloadEmbedding; | 1 | uimsbf |
| SaocSpecificConfig(); |  |  |
| break; |  |  |
| default: |  |  |
| /* reserved */ |  |  |
| } |  |  |
| … |  |  |
| } |  |  |

After subclause 1.6.2.1.17 add the new subclause 1.6.2.1.18 as follows:

1.6.2.1.18	SaocSpecificConfig

Defined in ISO/IEC 23003-2 subclause 5.1.

In subclause 1.6.2.2.1 extend Table 1.17 “Audio Object Types” as follows:

Table 1.17 — Audio Object Types

| Object Type ID | Audio Object Type | definition of elementary stream payloads and detailed syntax | Mapping of audio payloads to access units and elementary streams |
| --- | --- | --- | --- |
| 0 | NULL |  |  |
| … |  |  |  |
| 41 | SMR Main | ISO/IEC 14496-23 |  |
| 42 | (reserved) |  |  |
| 43 | SAOC | ISO/IEC 23003-2 |  |

After subclause 1.6.3.17, add a new subclause 1.6.3.18 as follows:

### 1.6.3.18	saocPayloadEmbedding

The audio Object Type ID 43 SAOC is used to convey spatial audio object coding side information for SAOC decoding as defined in ISO/IEC 23003-2. Depending on this flag, the SAOC data payload, i.e., SAOCFrame(), is available by different means:

Table 1.22A – saocPayloadEmbedding

| saocPayloadEmbedding | Meaning |
| --- | --- |
| 0 | One SAOCFrame() is mapped into one access unit. Subsequent access units form one elementary stream. That elementary stream will always depend on another elementary stream that contains the underlying (downmixed) audio data. |
| 1 | The top level payload is multiplexed into the underlying (downmixed) audio data. The actual multiplexing details depend on the presentation of the audio data (i.e., usually on the AOT). Note that this leads to an elementary stream with no real payload. That elementary stream will always depend on another elementary stream that contains both, the underlying (downmixed) audio data and the multiplexed spatial audio data. |

In subclause 4.4.2.7 extend Table 4.57 “Syntax of extension_payload()” as follows:

Table 4.57 – Syntax of extension_payload()

| Syntax | No. of bits | Mnemonic |
| --- | --- | --- |
| extension_payload(cnt) |  |  |
| { |  |  |
| extension_type; | 4 | uimsbf |
| align = 4; |  |  |
| switch( extension_type ) { |  |  |
| case EXT_DYNAMIC_RANGE: |  |  |
| return dynamic_range_info(); |  |  |
| case EXT_SAC_DATA: |  |  |
| return sac_extension_data(cnt); |  |  |
| case EXT_SAOC_DATA: |  |  |
| return saoc_extension_data(cnt); |  |  |
| case EXT_SBR_DATA: |  |  |
| return sbr_extension_data(id_aac, 0); |  | Note 1 |
| case EXT_SBR_DATA_CRC: |  |  |
| return sbr_extension_data(id_aac, 1); |  | Note 1 |
| case EXT_DATA_LENGTH: |  |  |
| hlp = 1; |  |  |
| len; | 4 | uimsbf |
| if (len==15) { |  |  |
| len += add_len; | 8 | uimsbf |
| hlp += 1; |  |  |
| If (add_len==255) { |  |  |
| len += add_add_len; | 16 | uimsbf |
| hlp += 2; |  |  |
| } } |  |  |
| return hlp+extension_payload(len); |  | Note 2 |
| case EXT_FILL_DATA: |  |  |
| fill_nibble; /* must be ‘0000’ */ | 4 | uimsbf |
| for (i=0; i<cnt-1; i++) { |  |  |
| fill_byte[i]; /* must be ‘10100101’ */ | 8 | uimsbf |
| } |  |  |
| return cnt; |  |  |
| case EXT_DATA_ELEMENT: |  |  |
| data_element_version; | 4 | uimsbf |
| switch( data_element_version ) { |  |  |
| case ANC_DATA: |  |  |
| loopCounter = 0; |  |  |
| dataElementLength = 0; |  |  |
| do { |  |  |
| dataElementLengthPart; | 8 | uimsbf |
| dataElementLength += dataElementLengthPart; |  |  |
| loopCounter++; |  |  |
| } while (dataElementLengthPart == 255); |  |  |
| for (i=0; i<dataElementLength; i++) { |  |  |
| data_element_byte[i]; | 8 | uimsbf |
| } |  |  |
| return (dataElementLength+loopCounter+1); |  |  |
| default: |  |  |
| align = 0; |  |  |
| } |  |  |
| case EXT_FIL: |  |  |
| default: |  |  |
| for (i=0; i<8*(cnt-1)+align; i++) { |  |  |
| other_bits[i]; | 1 | uimsbf |
| } |  |  |
| return cnt; |  |  |
| } |  |  |
| } |  |  |
| Note 1: id_aac is the id_syn_ele of the corresponding AAC element (ID_SCE or ID_CPE) or ID_SCE in case of CCE. Note 2: The extension_payload() included here must not have extension_type == EXT_DATA_LENGTH. |

In subclause 4.4.2.7 after Table 4.61 add a new Table 4.61A “saoc_extension_data()” as given below:

Table 4.61A – Syntax of saoc_extension_data()

| Syntax | No. of bits | Mnemonic |
| --- | --- | --- |
| saoc_extension_data(cnt) |  |  |
| { |  |  |
| ancType; | 2 | uimsbf |
| ancStart; | 1 | uimsbf |
| ancStop; | 1 | uimsbf |
| for (i=0; i<cnt-1; i++) { |  |  |
| ancDataSegmentByte[i]; | 8 | bslbf |
| } |  |  |
| return (cnt); |  |  |
| } |  |  |

In subclause 4.5.2.9.3 extend Table 4.121 “Values of the extension_type field” as follows:

Table 4.121 – Values of the extension_type field

| Symbol | Value of extension_type | Purpose |
| --- | --- | --- |
| EXT_FILL | ‘0000’ | bitstream payload filler |
| EXT_FILL_DATA | ‘0001’ | bitstream payload data as filler |
| EXT_DATA_ELEMENT | ’0010‘ | data element |
| EXT_DATA_LENGTH | ‘0011’ | container with explicit length for extension_payload() |
| EXT_SAOC_DATA | ‘1010’ | SAOC |
| EXT_DYNAMIC_RANGE | ‘1011’ | dynamic range control |
| EXT_SAC_DATA | ‘1100’ | MPEG Surround |
| EXT_SBR_DATA | ‘1101’ | SBR enhancement |
| EXT_SBR_DATA_CRC | ‘1110’ | SBR enhancement with CRC |
| - | all other values | Reserved: These values can be used for a further extension of the syntax in a compatible way. |
| Note: Extension payloads of the type EXT_FILL or EXT_FILL_DATA have to be added to the bitstream payload if the total bits for all audio data together with all additional data are lower than the minimum allowed number of bits in this frame necessary to reach the target bitrate. Those extension payloads are avoided under normal conditions and free bits are used to fill up the bit reservoir. Those extension payloads are written only if the bit reservoir is full. |

After subclause 4.5.2.11 add a new subclause 4.5.2.12 as given below:

#### 4.5.2.12	Spatial Audio Object Coding (SAOC)

The syntax element saoc_extension_data() is used to embed spatial audio object coding side information for SAOC decoding as defined in ISO/IEC 23003-2. The semantics of the syntax elements ancType, ancStart, ancStop, and ancDataSegmentByte is defined in ISO/IEC 23003-2 subclause 7.2.4.

In subclause 4.5.5 Figures, add in Table 4.149 “AAC error sensitivity category assignment for extended payload and low delay sbr payload” the following entries:

Table 4.149 – AAC error sensitivity category assignment for extended payload and low delay sbr payload

| extension_payload | low delay sbr payload | data_element | function |
| --- | --- | --- | --- |
| 5 | - | len | extension_payload() |
| 5 | - | add_len | extension_payload() |
| 5 | - | add_add_len | extension_payload() |

In subclause 4.5.5 Figures, change Figure 4.26 “Dependency structure in the case of ER multichannel AAC ELD syntax (channelConfiguration == 6)” as follows:

Figure 4.1 – Dependency structure in the case of ER multichannel AAC ELD syntax (channelConfiguration == 6).

In subclause 4.6.20.3 extend Table 4.180 “Syntax of ELDSpecificConfig()” as follows:

Table 4.180 – Syntax of ELDSpecificConfig ()

In subclause 4.6.20.4 extend Table 4.182 “ELD extension_type” as follows:

Table 4.182 – Values of the eldExtType field

| Symbol | Value of eldExtType | Purpose |
| --- | --- | --- |
| ELDEXT_TERM | ‘0000’ | Termination tag |
| ELDEXT_SAOC | ‘0001’ | SAOC config |
| /* reserved */ | ‘0010’ | /* reserved */ |
| … | … | … |
| /* reserved */ | ‘1111’ | /* reserved */ |